## Slide 1: Standards & Regulations Presentation ISO 10993 & ISO 13485
Team C: Kaushik Balasundar, Parker Hill, Anthony Kyu, Sundaram Seivur, Gunjan Sethi

## Slide 2: ISO 10993
Biological Evaluation of Medical Devices

## Slide 3: What is it about?
Goal: Protect humans from potential biological risks arising from the use of medical devices
Provides a framework in which to plan a biological evaluation and evaluate the resulting risks
Not a rigid test plan, experts must plan tests themselves
Evaluation should include consideration of:
Medical device geometry
Area of application
Materials
Physical and chemical characteristics
History of clinical or human use
Toxicology or biological safety data
Test procedures

## Slide 4: Why should we care? [Biocompatibility Issues]
Biocompatibility: ability of a medical device or material to perform with an appropriate host response in a specific application
Potential unwanted host responses could include blood clotting, inflammation, local tissue degradation, etc.
Furthemore, if a device is not biostable, it could lead to premature degradation due to wear
Medical Devices: any instrument, apparatus, implement, machine, appliance, implant, or reagent intended by a manufactured to be used on human beings for medical purposes

## Slide 5: Product Application
Applies to evaluation of materials and medical devices that are expected to have direct or indirect contact with –
Patient’s Body
User’s Body
Nature of Contact
Non-contacting?
Surface only?
Externally communicating?
Implants?
Duration of Contact
Upto 24 hrs?
24 hrs - 30 days?
> 30 days?
Transitory contant?
Think about the product’s..

## Slide 6: Main Prescriptions: Biological Evaluation and Risk Analysis

## Slide 7: Main Prescriptions: Biological Tests

## Slide 8: Application to ARTHuR
Components to test for biocompatibility:
Reamer head (stainless steel)
Marker holder (stainless steel)
Probe (stainless steel)
Other potential considerations for THR:
Femoral stem (coarse titanium)
Acetabular cup (coarse titanium)
Bone screws (stainless steel)
Femoral head (ceramic)
Inner acetabular cup (polyethylene)

## Slide 9: ISO 13485
Medical devices — Quality Management Systems

## Slide 10: What is it about?
A quality management system (QMS) is a set of policies, processes and procedures that help an organization meet the requirements expected by its stakeholders.
ISO 13485 is designed to be used by organizations throughout the life cycle of a medical device, from initial conception to production and post-production, including final decommission and disposal.

## Slide 11: Product Application
Conceptualization → Production → Post-production → Decommission → Disposal
  It also covers aspects such as storage, distribution, installation and servicing, and the provision of associated services.
The standard can be used by internal and external parties, such as certification bodies, to help them with their certification processes, or by supply chain organizations that are required by contract to conform.
Applicable to a wide range of medical equipment such as wound dressings, implantable devices, and software controlled devices such as CT scanners etc.

## Slide 12: Main Prescriptions: General Requirements
The organization shall
  document a QMS and maintain its effectiveness
  Apply a risk based approach to the control of the appropriate processes
  Determine the sequence and interaction of these processes
When the organization chooses to outsource any processes, it shall monitor and ensure control over such processes
The organization shall document procedures for the validation of the application of computer software used in the quality management system

## Slide 13: Main Prescriptions: Documentation Requirements
The quality management system documentation shall include:
a) documented statements of a quality policy and quality objectives;
b) a quality manual;
c) documented procedures and records required by this International Standard;
d) documents, including records, determined by the organization to be necessary to ensure the effective planning, operation, and control of its processes;
e) other documentation specified by applicable regulatory requirements.

## Slide 14: Main Prescriptions: Management Responsibility
Top management commitment
  Evidence of development, evidence and maintenance of QMS
Ensuring customer requirements development & compliance
Planning to establish quality standards at all levels & functions
Responsibility, authority and communication
  Personnel who have authority to ensure compliance with quality standards
  Reports structure
  Appropriate communication structure to ensure traceability of issues
Procedures for management reviews
  System to get reviews at all levels
  Protocols for remedial outputs
Notes: Top Management Commitment will need to ensure the following:
In the form of centralized meetings, address the importance of a QMS
Conducting reviews to ensure they are followed
Ensuring availability of resources
Protocol for meeting customer requirements
Legal bounds to commitment to quality policy
They will need to ensure customer requirements are gathered, developed and complied to. This also involves enforcing necessary requirements not specified by the customer
Planning before the beginning of a project to ensure that there is a plan of action on how to comply with regulations
They will also need to set in place dedicated personnel in charge of quality assurance at various functions. The report structure in place will need to be documented for traceability
They need to also place procedures for management reviews to receive feedback and carry out remedial actions

## Slide 15: Main Prescriptions: Resource Management
Human resources
  Training, skills & experience
  Evaluate efficacy
  Maintain records of procedures undertaken
Infrastructure
  Buildings & workspaces
  Equipment for quality measurement
  Supporting physical & digital services
Work environment and contamination control
  Protocols for health, cleanliness and clothing of personnel
  Sterilization

## Slide 16: Application to ArTHUR
Project Planning
  Requirements development, documentation, and maintenance
  Trade studies
  Customer interviews & expert consultation with surgeons
Project management efforts
  Documentation control
  Clear ownerships & accountability
  Customer meetings and progress reviews
  Issue logs and code reviews
System Validation and Verification
  Exposing key system health & performance parameters
  Evaluation metrics for each sub-system at various stages
  Active watchdog sub-system for continuous monitoring & intervention
Controlled work environment, contamination control protocols, testing in later stages

## Slide 17
thanks!!!! ask me questions now.
i am biocompatible r u?