## Slide 1
Standards and Regulations
Team H : DockDockGo Sergi Widjaja, Siddhant Wadhwa, Sushanth Jayanth, Soham Bhave, Vineet Tambe
Notes: Good Evening everyone, we’re excited to be back here sharing our project’s latest status with you after a summery little break.

## Slide 2: Standards Chosen
ANSI RIA R15.08:2020
  American National Standard for Industrial Mobile Robots - Safety Requirements
ANSI RIA R15.06:2012
  American National Standard for Industrial Robots and Robot Systems - Safety Requirements

## Slide 3: ANSI RIA R15.08:2020 Industrial Mobile Robots

## Slide 4: Overview
Safety requirements for Industrial Mobile Robots (IMRs)
Describes the basic hazards associated with IMRs in industrial requirements.
Provides requirements to eliminate or adequately reduce the described risks
For structured and semi-structured environments with trained personnel

## Slide 5: Applicable Products and Market
Covers applications that are strictly industrial
  Manufacturing
  Laboratory
  Logistics
  Etc.
Covers autonomous and a subset of guided mobile robots
  Manually driven robots and/or instruments are explicitly excluded

## Slide 6: Different Types of IMRs
IMR Type A
No attachment
IMR Type B
Passive Attachment
IMR Type C
Active Attachment

## Slide 7: Main Prescription
Hazard analysis and risk assessment must be conducted conforming to the list of hazards outlined
Requirements must be derived from the standards
Risk assessment scope must encompass reasonably foreseeable misuse of a product
Decomposes risk reduction measures from supplier and user

## Slide 8: Main Prescriptions
Modes of operation (automatic, semi-automatic, & manual)
  Mobile platform are not permitted to operate in automatic mode if attachment is in manual mode, vice versa
  Modes should be explicitly indicated
Control functions (e-stop, protective stop, etc)
  Shall not impose sudden movements on the robot that might cause additional hazard
  Automatic restart is permitted when obstacles are no longer visible
Navigation and control
  Replanning should happen continually without hazards (dynamic obstacles, etc.)
  Collision avoidance function should include the base platform and the attachment
  Mobile manipulator velocity limiting must take into account the base platforms’ characteristics
  Loss of localization must be handled gracefully

## Slide 9: Application to Our Project
Project Attributes | Requirements derived by the standards
Neobotix control modes | Control mode must be explicitly indicated
 | Automatic restart when obstacles are no longer on the path of the AMR
 | Switching modes must not impose sudden movements
Navigation functions | Replanning happens continuously without hazard
 | Collision model must be derived from the mobile platform and the attachment
 | Loss of localization must be handled gracefully

## Slide 10: ANSI RIA R15.06:2012 Industrial Mobile Robots

## Slide 11: Main Prescription
Risk assessment and Hazard Identification
Design Requirements
Verification and Validation
Information for Use

## Slide 12: Main Prescription
Perform risk assessment to enable systematic analysis and evaluation of the risks associated with the robot system over its whole life cycle.
Risk assessment should include -
  Determination of limits of the system (Use limits, time limits, space limits, etc.)
  Hazard Identification (Mechanical, Electrical, Themal, etc.)
  Risk estimation & Evaluation

## Slide 13: Main Prescription
Identified risks shall be eliminated or reduced first by design or by substitution, then by safeguarding and other complementary measures
Design Requirements:
  General Requirements
  Actuating Controls Requirements
  Safety-related Control Requirements
  Robot Stopping Functions
  Speed Control
  Operation Modes
  Multi-robot Requirements
  Collaborative Requirements

## Slide 14: Main Prescription
Verification and Validation
  Visual Inspection
  Practical Tests
  Observation during operation
  Reviews of design, risk assessment
Information of Use
  Information and instructions necessary for the correct use of the system
  Information and warnings to the user about any residual risks.
  Information for use from component machine manufacturers

## Slide 15: Application to Our Project
Project Attributes | Requirements derived by the standards
Embedded compute on the robot | Live electrical elements must be covered to avoid safety hazards
Navigate around the mezzanine area | Define safety zones where the robots operate and ensure measures are in place to prevent them from leaving these areas.
Means of e-stop initiation | User must have quick and unobstructed access to the e-stop means
Multi-robot planning and control | All robots must normally be in the same state during simultaneous operation.
 | Robot must be selected before it can be moved
Human-robot interaction (HRI) interface | Robots designed for collaboration shall provide visual indication when the robot is in collaborative mode